Class Normalized Cross Correlation

Includes:
stdio.h
math.h
“Matrix.h”

Methods:
NormalizedCrossCorrelation();
void setTemplate(int _wh) { template_width = _wh; template_height = _wh; };
void setTemplate(int _w, int _h) { template_width = _w; template_height = _h; };
void setSearchWindow(int _wh) { search_window_width = _wh; search_window_height = _wh; };
void setSearchWindow(int _w, int _h) { search_window_width = _w; search_window_height = _h; };
void setTemplateCenter(int _x, int _y) { template_center_x = _x; template_center_y = _y; };
void setSearchWindowCenter(int _x, int _y) { search_window_center_x = _x; search_window_center_y = _y; };
int searchHomologous(Matrix *, Matrix *);
double directCorrelation(Matrix *X, Matrix *Y, int template_cx, int template_cy, int matching_cx, int matching_cy);
double getBestP() { return best_p; };
int getBestX() { return best_x; };
int getBestY() { return best_y; };
void setMinStd(double _mstd) { min_std_acceptance = _mstd; };
bool checkTemplateStd(Matrix *refmat);

Methods description:

Genaral notes:
Matrices are images ranging from 0.0 to 1.0.

setTemplate
Set template size.
User may set both width and height at the same size or use different sizes.

setSearchWindow
Set search window size.
User may set both width and height at the same size or use different sizes.

setTemplateCenter
Specifies the coordinates of the template center.

setSearchWindowCenter
Specifies the coordinates of the search window center.

searchHomologous
Match matrices images M1 and M2.
M1 is the reference, and M2 the searching image.
All the previous parameters must be set before running this method.

directCorrelation
Calculate the direct correlation only in a given match window (window inside search window).
User must set the size of the template before running this method.

getBestP
After running searchHomologous(), informs the best pearson coefficient found.

getBestX
After running searchHomologous(), informs the best column coordinate found.

getBestY
After running searchHomologous(), informs the best row coordinate found.

setMinStd
Set the minimum template standard deviation evaluation.
This method is useful to check if the template is ready to be correlated.
Works with checkTemplateStd().

checkTemplateStd
Check the template standard deviation.

The E-FOTO Team

Class developed by: Marcelo Teixeira Silveira
Document: Marcelo Teixeira Silveira
Date: 2011-2012