Class Least Squares Matching

Includes:
stdio.h
math.h
“Matrix.h”
“NormalizedCrossCorrelation.h”

Methods:
LeastSquaresMatching();
enum filterType { Gradient, Prewitt, Sobel };
int searchHomologous(Matrix *img1, Matrix *img2, double Tx, double Ty, double Mx, double My);
void setTemplate(int _wh) { template_width = _wh; template_height = _wh; };
void setTemplate(int _w, int _h) { template_width = _w; template_height = _h; };
void setTemplateCenter(int _x, int _y) { template_center_x = _x; template_center_y = _y; };
void setMatchingWindowCenter(int _x, int _y) { matching_window_center_x = _x; matching_window_center_y = _y; };
void setGradientFilter(filterType _ft) { gradient_filter = _ft; };
int searchHomologous(Matrix *M1, Matrix *M2);
double getBestP() { return best_p; };
double getBestX() { return best_x; };
double getBestY() { return best_y; };
Matrix& getAffineParameters() { return affine_coefficients; };
void setMinStd(double _mstd) { ncc.setMinStd(_mstd); };
void setMaxIterations(int _its) { max_iterations = _its; };
void getNextPosition(double *x, double *y, int step_x, int step_y);
void setConvergenceLimits(double _shift, double _scale, double _shear) { limit_shift_values = _shift; limit_scale_values = _scale; limit_shear_values = _shear; };

Methods description:

Genaral notes:
Matrices are images ranging from 0.0 to 1.0.
This class has a built in filter methods, which are not used.

setTemplate
Set template size.
User may set both width and height at the same size or using different sizes.

setTemplateCenter
Specifies the coordinates of the template center.

setMatchingWindowCenter
Specifies the coordinates of the matching window center.

searchHomologous
Match matrices images M1 and M2.
M1 is the reference, and M2 the searching image.
All the previous parameters must be set before running this method.

setGradientFilter
Set gradient filter type, according to filterType.
This method is not being used by the LSM.

getBestP
After running searchHomologous(), informs the best pearson coefficient found.

getBestX
After running searchHomologous(), informs the best column coordinate found.

getBestY
After running searchHomologous(), informs the best row coordinate found.

setMinStd
Set the minimum template standard deviation evaluation.
This method is useful to check if the template is ready to be correlated.
Works with checkTemplateStd().

checkTemplateStd
Check the template standard deviation.

setMaxIterations
Set the maximum number of iterations. Default is 10.

getAffineParameters
Return the affine parameters (a0, a1, a2, b0, b1, b2) in a 6x1 matrix.

checkTemplateStd
Check the template standard deviation.

SetConvergenceLimits
Change the limits of convergence shift acceptance between iterations.
Default:
shift: 0.05
scale: 0.01
shear: 0.01
Shift parameters: a0, b0
Scale parameters: a2, b1
Shear parameters: a1, b2
Please, see “Digital Photogrammetry”, T. Schenk, Terra Science, 1999, chapter 10, for more datails.
Schenk considers affine parameters (t0, t1, t2, t3, t4, t5) instead of (a0, a1, a2, b0, b1, b2).

The E-FOTO Team

Class developed by: Marcelo Teixeira Silveira
Document: Marcelo Teixeira Silveira
Date: 2011-2012