Class Dem Grid

Includes:
stdio.h
math.h
string
iostream
fstream
"MatchingPoints.h"
"MatchingPointsGrid.h"
"Matrix.h"

Methods:
DemGrid(double, double, double, double, double, double);
enum saveMode { efotoDEM, ascii };
void saveDem(char *, saveMode);
void loadDem(char *, saveMode);
void createNewGrid(double, double, double, double, double, double);
void changeGridResolution(double, double);
void interpolateNearestPoint();
void interpolateMovingAverage(double, double, int);
void interpolateTrendSurface(int);
void interpolateMovingSurface(double, double, int, int);
void setPointList(MatchingPointsList *);
double getElapsedTime() { return elap_time; };
void cutGrid(double min, double max, bool fromList);
void getMinMax(double &, double &);
double getHeightXY(double X, double Y);
double getHeight(double col, double row);
Matrix *getDemImage(double min=0.0, double max=0.0);

Methods description:

Genaral notes:
Images ranging from 0.0 to 1.0.

saveDem / loadDem
Save / load DEM acoording to the following formats:
efotoDEM – binary file.
ascii – Text file.

createNewGrid(Xi, Yi, Xf, Yf, res_x, res_y)
Define a new grid.

changeGridResolution(res_x, res_y)
Change grid resolution.

interpolateNearestPoint
Interpolate cloud of points given by setPointList method, using Nearest Point.

interpolateMovingAverage
Interpolate cloud of points given by setPointList method, using Moving Average.

interpolateTrendSurface
Interpolate cloud of points given by setPointList method, using Trend Surface.

InterpolateMoving Surface
Interpolate cloud of points given by setPointList method, using Moving Surface.

setPointList
Link a 3D cloud of point list. This points are resulted from matching.

getElapsedTime
Return the time tooked in interpolations. Only in Unix/Linux.

cutGrid
Cut grid from min height to max height, filling with 0.0 the heights outside this range.

getMinMax
Retuns the minimum and maximum values of height.

getHeightXY
Returns the interpolated height for a given X,Y coordinate. Bilinear interpolation is used.

getHeight
Returns the interpolated height for a given col,row grid coordinate. Bilinear interpolation is used.

getDemImage
Returns DEM image matrix, ranging from 0.0 to 1.0. User may define min and max height for enhancing image contrast.

getDem
Returns a copy of DEM as a matrix.